## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 2
David Money Harris and Sarah L. Harris

## Slide 2
Introduction
Boolean Equations
Boolean Algebra
From Logic to Gates
Multilevel Combinational Logic
X’s and Z’s, Oh My
Karnaugh Maps
Combinational Building Blocks
Timing
Chapter 2 :: Topics

## Slide 3
A logic circuit is composed of:
Inputs
Outputs
Functional specification
Timing specification
Introduction

## Slide 4
Nodes
  Inputs: A, B, C
  Outputs: Y, Z
  Internal: n1
Circuit elements
  E1, E2, E3
  Each a circuit
Circuits

## Slide 5
Combinational Logic
  Memoryless
  Outputs determined by current values of inputs
Sequential Logic
  Has memory
  Outputs determined by previous and current values of inputs
Types of Logic Circuits

## Slide 6
Every element is combinational
Every node is either an input or connects to exactly one output
The circuit contains no cyclic paths
Example:
Rules of Combinational Composition

## Slide 7
Functional specification of outputs in terms of inputs
Example: S = F(A, B, Cin)
Cout = F(A, B, Cin)
Boolean Equations

## Slide 8
Complement: variable with a bar over it
A, B, C
Literal: variable or its complement
A, A, B, B, C, C
Implicant: product of literals
ABC, AC, BC
Minterm: product that includes all input variables
ABC, ABC, ABC
Maxterm: sum that includes all input variables
(A+B+C), (A+B+C), (A+B+C)
Some Definitions

## Slide 9: Sum-of-Products Form
Sum-of-Products (SOP) Form
All Boolean equations can be written in SOP form
Each row has a minterm

## Slide 10: Sum-of-Products Form
Sum-of-Products (SOP) Form
All Boolean equations can be written in SOP form
Each row has a minterm
A minterm is a product (AND) of literals
Each minterm is TRUE for that row (and only that row)

## Slide 11: Sum-of-Products Form
Y = F(A, B) = AB + AB
Sum-of-Products (SOP) Form
All Boolean equations can be written in SOP form
Each row has a minterm
A minterm is a product (AND) of literals
Each minterm is TRUE for that row (and only that row)
Form function by ORing minterms where output is 1
Thus, a sum (OR) of products (AND terms)

## Slide 12: Sum-of-Products Form
Y = F(A, B) = AB + AB = Σ(1, 3)
Sum-of-Products (SOP) Form
All equations can be written in SOP form
Each row has a minterm
A minterm is a product (AND) of literals
Each minterm is TRUE for that row (and only that row)
Form function by ORing minterms where output is 1
Thus, a sum (OR) of products (AND terms)

## Slide 13
All Boolean equations can be written in POS form
Each row has a maxterm
Product-of-Sums (POS) Form

## Slide 14
All Boolean equations can be written in POS form
Each row has a maxterm
A maxterm is a sum (OR) of literals
Each maxterm is FALSE for that row (and only that row)
Product-of-Sums (POS) Form

## Slide 15
Y = F(A, B) = (A + B)●(A + B)
All Boolean equations can be written in POS form
Each row has a maxterm
A maxterm is a sum (OR) of literals
Each maxterm is FALSE for that row (and only that row)
Form function by ANDing maxterms where output is 0
Thus, a product (AND) of sums (OR terms)
Product-of-Sums (POS) Form

## Slide 16
Y = F(A, B) = (A + B)(A + B) = Π(0, 2)
All Boolean equations can be written in POS form
Each row has a maxterm
A maxterm is a sum (OR) of literals
Each maxterm is FALSE for that row (and only that row)
Form function by ANDing maxterms where output is 0
Thus, a product (AND) of sums (OR terms)
Product-of-Sums (POS) Form

## Slide 17
You are going to the cafeteria for lunch
  You won’t eat lunch (E = 0)
  If it’s not open (O = 0) or
  If they only serve corndogs (C = 1)
Write a truth table for determining if you will eat lunch (E).
Boolean Equations Example

## Slide 18
You are going to the cafeteria for lunch
  You won’t eat lunch (E = 0)
  If it’s not open (O = 0) or
  If they only serve corndogs (C = 1)
Write a truth table for determining if you will eat lunch (E).
Boolean Equations Example

## Slide 19
SOP – sum-of-products
POS – product-of-sums
SOP & POS Form

## Slide 20
SOP – sum-of-products
POS – product-of-sums
E = (O + C)(O + C)(O + C)
= Π(0, 1, 3)
E = OC
= Σ(2)
SOP & POS Form

## Slide 21
Boolean Algebra
Axioms and theorems to simplify Boolean equations
Like regular algebra, but simpler: variables have only two values (1 or 0)
Duality in axioms and theorems:
  ANDs and ORs, 0’s and 1’s interchanged

## Slide 22
Boolean Axioms
Number | Axiom | Name
A1 | B = 0 if B ≠ 1 | Binary Field
A2 | 0 = 1 | NOT
A3 | 0 • 0 = 0 | AND/OR
A4 | 1 • 1 = 1 | AND/OR
A5 | 0 • 1 = 1 • 0 = 0 | AND/OR

## Slide 23
Dual: Replace: • with +
0 with 1
Boolean Axioms
Number | Axiom | Name
A1 | B = 0 if B ≠ 1 | Binary Field
A2 | 0 = 1 | NOT
A3 | 0 • 0 = 0 | AND/OR
A4 | 1 • 1 = 1 | AND/OR
A5 | 0 • 1 = 1 • 0 = 0 | AND/OR

## Slide 24
Number | Axiom | Dual | Name
A1 | B = 0 if B ≠ 1 | B = 1 if B ≠ 0 | Binary Field
A2 | 0 = 1 | 1 = 0 | NOT
A3 | 0 • 0 = 0 | 1 + 1 = 1 | AND/OR
A4 | 1 • 1 = 1 | 0 + 0 = 0 | AND/OR
A5 | 0 • 1 = 1 • 0 = 0 | 1 + 0 = 0 + 1 = 1 | AND/OR
Dual: Replace: • with +
0 with 1
Boolean Axioms

## Slide 25
Boolean Theorems of One Variable
Number | Theorem | Name
T1 | B • 1 = B | Identity
T2 | B • 0 = 0 | Null Element
T3 | B • B = B | Idempotency
T4 | B = B | Involution
T5 | B • B = 0 | Complements

## Slide 26
Number | Theorem | Name
T1 | B • 1 = B | Identity
T2 | B • 0 = 0 | Null Element
T3 | B • B = B | Idempotency
T4 | B = B | Involution
T5 | B • B = 0 | Complements
Dual: Replace: • with +
0 with 1
Boolean Theorems of One Variable

## Slide 27
Number | Theorem | Dual | Name
T1 | B • 1 = B | B + 0 = B | Identity
T2 | B • 0 = 0 | B + 1 = 1 | Null Element
T3 | B • B = B | B + B = B | Idempotency
T4 | B = B |  | Involution
T5 | B • B = 0 | B + B = 1 | Complements
Dual: Replace: • with +
0 with 1
Boolean Theorems of One Variable

## Slide 28
B 1 = B
B + 0 = B
T1: Identity Theorem

## Slide 29
T1: Identity Theorem
B 1 = B
B + 0 = B

## Slide 30
B 0 = 0
B + 1 = 1
T2: Null Element Theorem

## Slide 31
T2: Null Element Theorem
B 0 = 0
B + 1 = 1

## Slide 32
B B = B
B + B = B
T3: Idempotency Theorem

## Slide 33
T3: Idempotency Theorem
B B = B
B + B = B

## Slide 34
B = B
T4: Identity Theorem

## Slide 35
T4: Identity Theorem
B = B

## Slide 36
B B = 0
B + B = 1
T5: Complement Theorem

## Slide 37
T5: Complement Theorem
B B = 0
B + B = 1

## Slide 38
Recap: Basic Boolean Theorems
Number | Theorem | Dual | Name
T1 | B • 1 = B | B + 0 = B | Identity
T2 | B • 0 = 0 | B + 1 = 1 | Null Element
T3 | B • B = B | B + B = B | Idempotency
T4 | B = B |  | Involution
T5 | B • B = 0 | B + B = 1 | Complements
Dual: Replace: • with +
0 with 1

## Slide 39
Boolean Theorems of Several Vars
Number | Theorem | Name
T6 | B•C = C•B | Commutativity
T7 | (B•C) • D = B • (C • D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | Distributivity
T9 | B• (B+C) = B | Covering
T10 | (B•C) + (B•C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | Consensus

## Slide 40
Boolean Theorems of Several Vars
Dual: Replace: • with +
0 with 1
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | Commutativity
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | Distributivity
T9 | B • (B+C) = B | B + (B•C) = B | Covering
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | (B+C) • (B+D) • (C+D) = (B+C) • (B+D) | Consensus

## Slide 41
Boolean Theorems of Several Vars
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | Commutativity
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | Distributivity
T9 | B • (B+C) = B | B + (B•C) = B | Covering
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | (B+C) • (B+D) • (C+D) = (B+C) • (B+D) | Consensus
Warning: T8’ differs from traditional algebra:
OR (+) distributes over AND (•)

## Slide 42
Boolean Theorems of Several Vars
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | Commutativity
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | Distributivity
T9 | B • (B+C) = B | B + (B•C) = B | Covering
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | (B+C) • (B+D) • (C+D) = (B+C) • (B+D) | Consensus
How do we prove these are true?

## Slide 43
How to Prove
Method 1: Perfect induction
Method 2: Use other theorems and axioms to simplify the equation
  Make one side of the equation look like the other

## Slide 44
Proof by Perfect Induction
Also called: proof by exhaustion
Check every possible input value
If the two expressions produce the same value for every possible input combination, the expressions are equal

## Slide 45
Example: Proof by Perfect Induction
Number | Theorem | Name
T6 | B•C = C•B | Commutativity
0 0
0 1
1 0
1 1
B C BC CB

## Slide 46
0 0
0 0
0 0
1 1
Number | Theorem | Name
T6 | B•C = C•B | Commutativity
Example: Proof by Perfect Induction
0 0
0 1
1 0
1 1
B C BC CB

## Slide 47
Boolean Theorems of Several Vars
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | Commutativity
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | Distributivity
T9 | B • (B+C) = B | B + (B•C) = B | Covering
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | (B+C) • (B+D) • (C+D) = (B+C) • (B+D) | Consensus
How do we prove these are true?

## Slide 48
T7: Associativity
Number | Theorem | Name
T7 | (B•C) • D = B • (C • D) | Associativity

## Slide 49
T8: Distributivity
Number | Theorem | Name
T8 | B • (C + D) = (B•C) + (B•D) | Distributivity

## Slide 50
T9: Covering
Number | Theorem | Name
T9 | B• (B+C) = B | Covering

## Slide 51
Prove true by:
Method 1: Perfect induction
Method 2: Using other theorems and axioms
Number | Theorem | Name
T9 | B• (B+C) = B | Covering
T9: Covering

## Slide 52
0 0
0 1
1 0
1 1
B C (B+C) B(B+C)
Method 1: Perfect Induction
Number | Theorem | Name
T9 | B• (B+C) = B | Covering
T9: Covering

## Slide 53
Method 1: Perfect Induction
0 0
1 0
1 1
1 1
Number | Theorem | Name
T9 | B• (B+C) = B | Covering
0 0
0 1
1 0
1 1
B C (B+C) B(B+C)
T9: Covering

## Slide 54
Method 1: Perfect Induction
0 0
1 0
1 1
1 1
Number | Theorem | Name
T9 | B• (B+C) = B | Covering
0 0
0 1
1 0
1 1
B C (B+C) B(B+C)
T9: Covering

## Slide 55
Number | Theorem | Name
T9 | B• (B+C) = B | Covering
Method 2: Prove true using other axioms and theorems.
T9: Covering

## Slide 56
Method 2: Prove true using other axioms and theorems.
B•(B+C) = B•B + B•C T8: Distributivity
= B + B•C T3: Idempotency
= B•(1 + C) T8: Distributivity
= B•(1) T2: Null element
= B T1: Identity
Number | Theorem | Name
T9 | B• (B+C) = B | Covering
T9: Covering

## Slide 57
T10: Combining
Prove true using other axioms and theorems:
Number | Theorem | Name
T10 | (B•C) + (B•C) = B | Combining

## Slide 58
Prove true using other axioms and theorems:
B•C + B•C = B•(C+C) T8: Distributivity
= B•(1) T5’: Complements
  = B T1: Identity
Number | Theorem | Name
T10 | (B•C) + (B•C) = B | Combining
T10: Combining

## Slide 59
T11: Consensus
Number | Theorem | Name
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | Consensus
Prove true using (1) perfect induction or (2) other axioms and theorems.

## Slide 60
Boolean Theorems of Several Vars
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | Commutativity
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | Distributivity
T9 | B • (B+C) = B | B + (B•C) = B | Covering
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | (B+C) • (B+D) • (C+D) = (B+C) • (B+D) | Consensus
Axioms and theorems are useful for simplifying equations.

## Slide 61
Simplifying an Equation
Reducing an equation to the fewest number of implicants, where each implicant has the fewest literals

## Slide 62
Simplifying an Equation
Reducing an equation to the fewest number of implicants, where each implicant has the fewest literals
  Recall:
  Implicant: product of literals
  ABC, AC, BC
  Literal: variable or its complement
A, A, B, B, C, C

## Slide 63
Simplifying an Equation
Reducing an equation to the fewest number of implicants, where each implicant has the fewest literals
  Recall:
  Implicant: product of literals
  ABC, AC, BC
  Literal: variable or its complement
A, A, B, B, C, C
Simplifying the equation is also called minimizing the equation

## Slide 64
Simplification methods
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P

## Slide 65
Simplification methods
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A

## Slide 66
Simplification methods
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A
“Simplification” theorem PA + A = P + A
    PA + A = P + A

## Slide 67
Proving the “Simplification” Theorem
“Simplification” theorem
PA + A = P + A
Method 1: PA + A = PA + (A + AP) T9’ Covering
= PA + PA + A T6 Commutativity
= P(A + A) + A T8 Distributivity
= P(1) + A T5’ Complements
= P + A T1 Identity

## Slide 68
“Simplification” theorem
PA + A = P + A
Method 2: PA + A = (A + A) (A + P) T8’ Distributivity
= 1(A + P) T5’ Complements
= A + P T1 Identity
Proving the “Simplification” Theorem

## Slide 69
T11: Consensus
Number | Theorem | Name
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | Consensus
Prove using other theorems and axioms:

## Slide 70
T11: Consensus
Number | Theorem | Name
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | Consensus
Prove using other theorems and axioms:
B•C + B•D + C•D
= BC + BD + (CDB+CDB) T10: Combining
= BC + BD + BCD+BCD T6: Commutativity
= BC + BCD + BD + BCD T6: Commutativity
= (BC + BCD) + (BD + BCD) T7: Associativity
= BC + BD T9’: Covering

## Slide 71
Boolean Theorems of Several Vars
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | Commutativity
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | Distributivity
T9 | B • (B+C) = B | B + (B•C) = B | Covering
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | (B+C) • (B+D) • (C+D) = (B+C) • (B+D) | Consensus

## Slide 72
Simplification methods
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A
“Simplification” theorem PA + A = P + A
    PA + A = P + A

## Slide 73
Y = AB + AB
Simplifying Boolean Equations
Example 1:

## Slide 74
Y = AB + AB
Y = A T10: Combining
or
= A(B + B) T8: Distributivity
= A(1) T5’: Complements
= A T1: Identity
Simplifying Boolean Equations
Example 1:

## Slide 75
Simplification methods
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A
“Simplification” theorem PA + A = P + A
    PA + A = P + A

## Slide 76
Y = A(AB + ABC)
Example 2:
Simplifying Boolean Equations

## Slide 77
Y = A(AB + ABC)
= A(AB(1 + C)) T8: Distributivity
= A(AB(1)) T2’: Null Element
= A(AB) T1: Identity
= (AA)B T7: Associativity
= AB T3: Idempotency
Example 2:
Simplifying Boolean Equations

## Slide 78
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A
“Simplification” theorem PA + A = P + A
    PA + A = P + A
Simplification methods

## Slide 79
Y = A’BC + A’ Recall: A’ = A
Example 3:
Simplifying Boolean Equations

## Slide 80
Y = A’BC + A’ Recall: A’ = A
Note:
A‘ is shorthand for A.
But use the tick symbol (‘) only when typing.
It’s easy to lose ticks (‘) when writing by hand!
It is strongly recommended that you simplify equations by writing by hand.
Example 3:
Simplifying Boolean Equations

## Slide 81
Y = A’BC + A’ Recall: A’ = A
= A’ T9’ Covering: X + XY = X
or
= A’(BC + 1) T8: Distributivity
= A’(1) T2’: Null Element
= A’ T1: Identity
Example 3:
Simplifying Boolean Equations

## Slide 82
Y = AB’C + ABC + A’BC
Example 4:
Simplifying Boolean Equations

## Slide 83
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A
“Simplification” theorem PA + A = P + A
    PA + A = P + A
Simplification methods

## Slide 84
Y = AB’C + ABC + A’BC
= AB’C + ABC + ABC + A’BC T3’: Idempotency
= (AB’C+ABC) + (ABC+A’BC) T7’: Associativity
= AC + BC T10: Combining
Example 4:
Simplifying Boolean Equations

## Slide 85
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A
“Simplification” theorem PA + A = P + A
    PA + A = P + A
Simplification methods

## Slide 86
Y = AB + BC +B’D’ + AC’D’
Method 1:
Y = AB + BC + B’D’ + (ABC’D’ + AB’C’D’) T10: Combining
= (AB + ABC’D’) + BC + (B’D’ + AB’C’D’) T6: Commutativity
T7: Associativity
= AB + BC + B’D’ T9: Covering
Method 2:
Y = AB + BC + B’D’ + AC’D’ + AD’ T11: Consensus
= AB + BC + B’D’ + AD’ T9: Covering
= AB + BC + B’D’ T11: Consensus
Example 5:
Simplifying Boolean Equations

## Slide 87
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A
“Simplification” theorem PA + A = P + A
    PA + A = P + A
Simplification methods

## Slide 88
Y = (A + BC)(A + DE)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Example 6:
Simplifying Boolean Equations

## Slide 89
Y = (A + BC)(A + DE)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: X = BC, Z = DE and rewrite equation
Y = (A+X)(A+Z) substitution (X=BC, Z=DE)
= A + XZ T8’: Distributivity
= A + BCDE substitution
or
Y = AA + ADE + ABC + BCDE T8: Distributivity
= A + ADE + ABC + BCDE T3: Idempotency
= A + ADE + ABC + BCDE
= A + ABC + BCDE T9’: Covering
= A + BCDE T9’: Covering
Example 6:
Simplifying Boolean Equations

## Slide 90
Y = (A + BC)(A + DE)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: X = BC, Z = DE and rewrite equation
Y = (A+X)(A+Z) substitution (X=BC, Z=DE)
= A + XZ T8’: Distributivity
= A + BCDE substitution
or
Y = AA + ADE + ABC + BCDE T8: Distributivity
= A + ADE + ABC + BCDE T3: Idempotency
= A + ADE + ABC + BCDE
= A + ABC + BCDE T9’: Covering
= A + BCDE T9’: Covering
Example 6:
Simplifying Boolean Equations
This is called
multiplying out
an expression to get
sum-of-products (SOP) form.

## Slide 91
SOP – sum-of-products
POS – product-of-sums
E = (O + C)(O + C)(O + C)
= Π(0, 1, 3)
E = OC
= Σ(2)
Review: Canonical SOP & POS Forms

## Slide 92
An expression is in sum-of-products (SOP) form when all products contain literals only.
SOP form: Y = AB + BC’ + DE
NOT SOP form: Y = DF + E(A’+B)
SOP form: Z = A + BC + DE’F
Multiplying Out: SOP Form

## Slide 93
Y = (A + C + D + E)(A + B)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: X = (C+D+E), Z = B and rewrite equation
Y = (A+X)(A+Z) substitution (X=(C+D+E), Z=B)
= A + XZ T8’: Distributivity
= A + (C+D+E)B substitution
= A + BC + BD + BE T8: Distributivity
or
Y = AA+AB+AC+BC+AD+BD+AE+BE T8: Distributivity
= A+AB+AC+AD+AE+BC+BD+BE T3: Idempotency
= A + BC + BD + BE T9’: Covering
Example:
Multiplying Out: SOP Form

## Slide 94
An expression is in product-of-sums (POS) form when all sums contain literals only.
POS form: Y = (A+B)(C+D)(E’+F)
NOT POS form: Y = (D+E)(F’+GH)
POS form: Z = A(B+C)(D+E’)
Canonical POS form: each product contains 1 of each literal.
Factoring: POS Form

## Slide 95
Y = (A + B’CDE)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: X = B’C, Z = DE and rewrite equation
Y = (A+XZ) substitution (X=B’C, Z=DE)
= (A+B’C)(A+DE) T8’: Distributivity
= (A+B’)(A+C)(A+D)(A+E) T8’: Distributivity
Example 1:
Factoring: POS Form

## Slide 96
Y = AB + C’DE + F
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: W = AB, X = C’, Z = DE and rewrite equation
Y = (W+XZ) + F substitution W = AB, X = C’, Z = DE
= (W+X)(W+Z) + F T8’: Distributivity
= (AB+C’)(AB+DE)+F substitution
= (A+C’)(B+C’)(AB+D)(AB+E)+F T8’: Distributivity
= (A+C’)(B+C’)(A+D)(B+D)(A+E)(B+E)+F T8’: Distributivity
= (A+C’+F)(B+C’+F)(A+D+F)(B+D+F)(A+E+F)(B+E+F) T8’: Distributivity
Example 2:
Factoring: POS Form

## Slide 97
DeMorgan’s Theorem
Number | Theorem | Name
T12 | B0•B1•B2… = B0+B1+B2… | DeMorgan’s Theorem

## Slide 98
DeMorgan’s Theorem
The complement of the product
is the
sum of the complements
Number | Theorem | Name
T12 | B0•B1•B2… = B0+B1+B2… | DeMorgan’s Theorem

## Slide 99
DeMorgan’s Theorem: Dual
# | Theorem | Dual | Name
T12 | B0•B1•B2… = B0+B1+B2… | B0+B1+B2… = B0•B1•B2… | DeMorgan’s Theorem
The complement of the product
is the
sum of the complements.
Dual: The complement of the sum
is the
product of the complements.

## Slide 100
Y = AB = A + B
Y = A + B = A B
DeMorgan’s Theorem

## Slide 101
Y = (A+BD)C
DeMorgan’s Theorem Example 1

## Slide 102
Y = (A+BD)C
= (A+BD) + C
= (A•(BD)) + C
= (A•(BD)) + C
= ABD + C
DeMorgan’s Theorem Example 1

## Slide 103
Y = (ACE+D) + B
DeMorgan’s Theorem Example 2

## Slide 104
Y = (ACE+D) + B
= (ACE+D) • B
= (ACE•D) • B
= ((AC+E)•D) • B
= ((AC+E)•D) • B
= (ACD + DE) • B
= ABCD + BDE
DeMorgan’s Theorem Example 2

## Slide 105
Y = AB = A + B
Y = A + B = A B
DeMorgan’s Theorem

## Slide 106
Backward:
  Body changes
  Adds bubbles to inputs
Forward:
  Body changes
  Adds bubble to output
Bubble Pushing

## Slide 107
What is the Boolean expression for this circuit?
Bubble Pushing

## Slide 108
What is the Boolean expression for this circuit?
Y = AB + CD
Bubble Pushing

## Slide 109
Begin at output, then work toward inputs
Push bubbles on final output back
Draw gates in a form so bubbles cancel
Bubble Pushing Rules

## Slide 110
Bubble Pushing Example

## Slide 111
Bubble Pushing Example

## Slide 112
Bubble Pushing Example

## Slide 113
Bubble Pushing Example

## Slide 114
Two-level logic: ANDs followed by ORs
Example: Y = ABC + ABC + ABC
From Logic to Gates

## Slide 115
Inputs on the left (or top)
Outputs on right (or bottom)
Gates flow from left to right
Straight wires are best
Circuit Schematics Rules

## Slide 116
Wires always connect at a T junction
A dot where wires cross indicates a connection between the wires
Wires crossing without a dot make no connection
Circuit Schematic Rules (cont.)

## Slide 117
Example: Priority Circuit
Output asserted
corresponding to
most significant
TRUE input
Multiple-Output Circuits

## Slide 118
Example: Priority Circuit
Output asserted
corresponding to
most significant
TRUE input
Multiple-Output Circuits

## Slide 119
Priority Circuit Hardware

## Slide 120
Don’t Cares

## Slide 121
Contention: circuit tries to drive output to 1 and 0
  Actual value somewhere in between
  Could be 0, 1, or in forbidden zone
  Might change with voltage, temperature, time, noise
  Often causes excessive power dissipation
Warnings:
  Contention usually indicates a bug.
  X is used for “don’t care” and contention - look at the context to tell them apart
Contention: X

## Slide 122
Floating, high impedance, open, high Z
Floating output might be 0, 1, or somewhere in between
  A voltmeter won’t indicate whether a node is floating
Tristate Buffer
Floating: Z

## Slide 123
Floating nodes are used in tristate busses
  Many different drivers
  Exactly one is active at
  once
Tristate Busses

## Slide 124
Boolean expressions can be minimized by combining terms
K-maps minimize equations graphically
PA + PA = P
Karnaugh Maps (K-Maps)

## Slide 125
Circle 1’s in adjacent squares
In Boolean expression, include only literals whose true and complement form are not in the circle
Y = AB
K-Map

## Slide 126
3-Input K-Map

## Slide 127
Y = AB + BC
3-Input K-Map

## Slide 128
Complement: variable with a bar over it
A, B, C
Literal: variable or its complement
A, A, B, B, C, C
Implicant: product of literals
ABC, AC, BC
Prime implicant: implicant corresponding to the largest circle in a K-map
K-Map Definitions

## Slide 129
Every 1 must be circled at least once
Each circle must span a power of 2 (i.e. 1, 2, 4) squares in each direction
Each circle must be as large as possible
A circle may wrap around the edges
Circle a “don't care” (X) only if it helps minimize the equation
K-Map Rules

## Slide 130
4-Input K-Map

## Slide 131
4-Input K-Map

## Slide 132
4-Input K-Map

## Slide 133
K-Maps with Don’t Cares

## Slide 134
K-Maps with Don’t Cares

## Slide 135
K-Maps with Don’t Cares

## Slide 136
Multiplexers
Decoders
Combinational Building Blocks

## Slide 137
Selects between one of N inputs to connect to output
log2N-bit select input – control input
Example: 2:1 Mux
Multiplexer (Mux)

## Slide 138
Logic gates
  Sum-of-products form
Tristates
  For an N-input mux, use N tristates
  Turn on exactly one to select the appropriate input
Multiplexer Implementations

## Slide 139
Using the mux as a lookup table
Logic using Multiplexers

## Slide 140
Reducing the size of the mux
Logic using Multiplexers

## Slide 141
N inputs, 2N outputs
One-hot outputs: only one output HIGH at once
Decoders

## Slide 142
Decoder Implementation

## Slide 143
OR the minterms
Logic Using Decoders

## Slide 144
Delay between input change and output changing
How to build fast circuits?
Timing

## Slide 145
Propagation delay: tpd = max delay from input to output
Contamination delay: tcd = min delay from input to output
Propagation & Contamination Delay

## Slide 146
Delay is caused by
  Capacitance and resistance in a circuit
  Speed of light limitation
Reasons why tpd and tcd may be different:
  Different rising and falling delays
  Multiple inputs and outputs, some of which are faster than others
  Circuits slow down when hot and speed up when cold
Propagation & Contamination Delay

## Slide 147
Critical (Long) Path: tpd = 2tpd_AND + tpd_OR
Short Path: tcd = tcd_AND
Critical (Long) & Short Paths

## Slide 148
When a single input change causes an output to change multiple times
Glitches

## Slide 149
What happens when A = 0, C = 1, B falls?
Glitch Example

## Slide 150
Glitch Example (cont.)

## Slide 151
Fixing the Glitch

## Slide 152
Why Understand Glitches?
Because of synchronous design conventions (see Chapter 3), glitches don’t cause problems.
It’s important to recognize a glitch: in simulations or on oscilloscope.
We can’t get rid of all glitches – simultaneous transitions on multiple inputs can also cause glitches.